22TON LOG SPLITTER

Log Splitter：Outdoor product that splits wood logs for

use as fuel in a fireplace or a woodstove.

Owner’s Manual and Operating Instructions

WARNING Read this manual. Serious injury or death can result if safety instructions are not followed.

Engine is shipped without oil. -Before starting engine, fill with SAE 10W-30 motor oil. -See engine manual for engine oil capacity. Hydraulic reservoir is shipped without oil. -When add oil, Verify oil level is 1from top of hydraulic reservoir (not including fill neck). Closely inspect all log splitter components. -If you have damaged components then: Contact the freight company that delivered the unit and file a claim.

Hazard Signal Word Definitions

|  | This is the safety alert symbol. It is used to alert you to potential personal injury hazards. Obey all safety messages that follow this symbol to avoid possible injury or death. |
| --- | --- |
|  | DANGER (red) indicates an imminently hazardous situation which, if not avoided, will result in death or serious injury. |
|  | WARNING (orange) indicates a potentially hazardous situation which, if not avoided, could result in death or serious injury. |
|  | CAUTION (yellow) indicates a potentially hazardous situation which, if not avoided, may result in minor or moderate injury. |
|  | CAUTION (yellow) used without the safety alert symbol indicates a potentially hazardous situation which, if not avoided, may result in property damage. |

1

Table of Contents

Important Safety Rules………………………………………………3,4

Machine Component Definitions………………….…………………5

Operation Instructions……………………………………………….6-9

Proper Operation of the Log Splitter………………………..6

How to split the log with slant surface………………………7

Horizontal and Vertical Operating Modes…………………..8

Driving Position…………………………………………….9

Maintenance and Storage……………………………………………10

Troubleshooting…………………….…………………………………….11

Specifications………………….………………………………………….12

Assembly Instruction……………………………………………………. 13-17

Parts Explosion…………………………………………………………..18-23

2

Important Safety Rules

WARNING 1.) Read this manual completely. Serious injury or death can result if safety instructions are not followed. Everyone who operates the log splitter must read and completely understand all safety rules, operating instructions, and maintenance instructions. You must be 16 or older to operate this machine. Keep untrained people away. -Shut engine off before leaving log splitter unattended. 2.) Crush hazard. Wedge can cut through skin and break bones. Keep both hands away from wedge and endplate. -Serious accidents can happen when other people are allowed inside the work zone. Keep everyone else out of the work zone while operating control valve. -Do not wear loose clothing. It can get tangled in moving parts of log splitter. -Only use the log splitter in daylight so you can see what you are doing. 3.) Flying objects. Pieces of log may fly out while splitting. Wear safety glasses. Serious eye injury can occur. 4.) Skin injection hazard. High pressure fluid can inject under skin resulting in serious injury including amputation. -Make sure all fittings are tight before applying pressure. Relieve system pressure before servicing. -Do not check for leaks with hand. Instead, use a piece of cardboard to check for leaks. -If skin injection happens, seek immediate “Surgical Treatment”. 5.) Towing hazard. Serious injury or death can occur if towing safety rules are not followed. -Review towing safety warnings in your towing vehicle manual. -Drive safely. Be aware of the added length of the log splitter. -Never ride or transport cargo on the log splitter. -Drive the vehicle with the log splitter securely attached. -Turn off the vehicle before leaving the log splitter unattended. -Choose a level surface to operate the log splitter. -Block the log splitter wheels to prevent unintended movement. -Never tow or operate this splitter while under the influence of alcohol, drugs, or medication.

Save These Instructions

3

Important Safety Rules

WARNING 6.) Risk of fire and explosion. Hot exhaust fumes from engine can cause fire. Gasoline is highly flammable and explosive. You can be burned or seriously injured when handling fuel. -Position muffler at least 7 feet from combustible objects. -Before adding fuel, stop the engine and keep heat, sparks, and flame away. Do not add fuel when engine is running or still hot. No smoking near engine. -Do not pump fuel directly into engine at gas station. Static charge can build and ignite fuel. Use a UL approved fuel container to transfer gas to the engine. Wipe up fuel spills immediately. -Only store and handle fuel outdoors. Gasoline vapors can ignite if they collect inside an enclosure. Explosion can result. -Do not change or add to exhaust system. Fire can result. -Do not change or add fuel tanks or fuel lines. Fire can result. -Before each use, check fuel tank and fuel lines for leaks. Any fuel leak is a fire hazard. Fix any fuel leaks before starting engine. -During transportation take precautions to make sure machine will not tip over and cause a fuel leak fire hazard. 7.) Breathing hazard. Poisonous fumes from engine can kill you. Do not operate indoors even if Ventilated. For outdoor use only.

CAUTION 1.) Hot muffler. You can be burned by muffler. Do not touch.

Save These Instructions

4

Machine Component Definitions

- Coupler. Attaches the log splitter to your vehicle. Fits only 50mm hitch balls.

- Hydraulic Cylinder. The hydraulic cylinder has a 4½” bore and a 23” stroke. It is rated to

3500 psi.

- Control Valve Handle. Use the control valve handle to move the wedge slide forward and backward.

- Wedge. The wedge features wedge wings and a taper that makes splitting easier.

- Log Cradle. Keeps the log on the beam without operator assistance.

- Cross Wedge. Fixed on the wedge with 1 Hex Bolts to make two types optional splitting.

- Beam. The beam is made of 6” wide flange beam (also called I-Beam).

- Engine. The air cooled engine powers the hydraulic pump.

- Tires with flange. Maximum rated speed is 25 Kilometre per hour.

- Two Stage Hydraulic Pump. The hydraulic pump makes the hydraulic oil flow through the system.

- Leg. The leg supports the log splitter while operating. The leg should be raised while towing (see Operation Instructions).

- Protection Tube.

5

Operation Instructions

Proper Operation of the Log Splitter

- Load a log onto the beam and against the endplate.

- Serious accidents can happen when other people are allowed inside the work zone. Keep everyone else out of the work zone while operating control valve.

- Make sure hands are clear of crush hazard zones.

- Push control valve handle FORWARD by two hands to split log.

- Push control valve handle BACKWARD by two hands to return wedge to its original position.

- Clear the split wood from the work zone.

WARNING Crush hazard. Wedge can cut through skin and break bones. Keep both hands away from wedge and beam slide. -Serious accidents can happen when other people are allowed inside the work zone. Keep everyone else out of the work zone while operating control valve. -Do not wear loose clothing. It can get tangled in moving parts of log splitter. -Only use the log splitter in daylight so you can see what you are doing.

6

Operation Instructions

HOW TO SPLIT THE LOG WITH SLANT SURFACE

7

Operation Instructions

8

Operation Instructions

WARNING Towing hazards. Serious injury or death can occur if towing safety rules are not followed. -Review towing safety warnings in your towing vehicle manual. -Drive safely. Be aware of the added length of the log splitter. -Never ride or transport cargo on the log splitter. -Drive the vehicle with the log splitter securely attached. -Turn off the vehicle before leaving the log splitter unattended. -Choose a level surface to operate the log splitter. -Block the log splitter wheels to prevent unintended movement. -Never tow or operate this log splitter while under the influence of alcohol, drugs, or medication.

9

Maintenance and Storage

Before performing maintenance, the log splitter must be placed in maintenance mode.

- Turn off engine.

- Move the control valve handle forward and backward to relieve hydraulic pressure.

After performing maintenance, make sure all guards, shields, and safety features are put back in place. Failure to follow this warning can result in serious injury.

Refer to the engine owner’s manual for engine maintenance.

| What | When | How |
| --- | --- | --- |
| Hoses | Each Use | Inspect for exposed wire mesh and leaks. Replace all worn or damaged hoses before starting engine |
| Hydraulic Fittings | Each Use | Inspect for cracks and leaks. Replace all damaged fittings before starting engine |
| Nuts and Bolts | Each Use | Check for loose bolts |
| Beam | Each Use | Apply grease to beam surface |
| Moving Parts | Each Use | Clear debris |

WARNING Skin injection hazard. High pressure fluid can inject under skin resulting in serious injury including amputation. -Make sure all fittings are tight before applying pressure. Relieve system pressure before servicing. -Do not check for leaks with hand. Instead, use a piece of cardboard to check for leaks. -If skin injection happens, seek immediate “Surgical Treatment”.

10

Troubleshooting

| Problem |  |
| --- | --- |
| Cylinder rod will not move | SOLUTION: A,D,E,H,J |
| Slow cylinder shaft speed when extending or retracting | SOLUTION: A,B,C,H,I,K,L |
| Wood will not split or splits extremely slowly | SOLUTION: A,B,C,F,I,K |
| Engine bogs down during splitting | SOLUTION: G,L |
| Engine stalls under low load condition | SOLUTION: D,E,L,M |
| Cause | Solution |
| A-Insufficient oil to pump | Check oil level in reservoir |
| B-Air in oil | Check oil level in reservoir |
| C-Excessive pump inlet vacuum | Check pump inlet hose for blockage or kinks |
| D-Blocked hydraulic lines | Flush and clean the splitter hydraulic system |
| E-Blocked control valve | Flush and clean the splitter hydraulic system |
| F-Low control valve setting | Adjust control valve with a pressure gauge |
| G-High control valve setting | Adjust control valve with a pressure gauge |
| H-Damaged control valve | Return control valve for authorized repair |
| I-Internal control valve leak | Return control valve for authorized repair |
| J-Internal cylinder leak | Return cylinder for authorized repair |
| K-Internally damaged cylinder | Return cylinder for authorized repair |
| L-Engine Control out of adjustment | Adjust idle control nuts |
| M-Engine is loaded during idle down mode | Use shorter log length (24” or less) to allow engine to speed up before contact. |

11

Specifications

12

ASSEMBLY

Step 1: Wheel Assembly

Attach the wheels (#63) to the oil tank axle (#51) secure using Flat Washer Ø20(58#), Hex Nut M20(59#), Cotter pin Ø4x36 (60#) and axle cap (61#).

Step 2: Attach Tow Bar and Support Leg

Fix the support leg (#92) to the tow bar (#98) by a pin (#91) and handle wheel (#93).

Step 3: Attached Tow Bar to the Oil Tank

Fix the tow bar to the oil tank by using 4 sets of hex bolt M12x40 (#99), flat washer Ø12 (#3) and lock nut M12 (#10).

13

Step 4: Assemble Rear Support Leg

Fix the rear support leg (#56) to the tow bar by using hex bolt M10x75 (#103), lock nut M10 (#44), flat washer Ø10(#43). Slide in hitch pin (#102) and secure with R pinØ3x55 (#97).

Step 5: Attach the Double Handle

.Loosen the Pin 5x26 (#36) and Cotter Pin Ø2x10 (#37), then attach the double handle assembly to the control valve using Pin 5x26 (#36), Cotter Pin Ø2x10 (#37), Lock Washer Ø8 (#76) and Inner Hex Bolt M8x16 (#34).

14

Step 6: Assemble Operating Handle to Control Valve and Assemble Tow Bar to the Beam.

Assemble the Beam to the tow bar, secure with cotter pin Ø4x40 (#101) & hitch pin (#100).

Step 7: Attach Engine

Assemble the engine (#78) to the oil tank by using hex bolt M8x75 (#104), flat washer Ø8 (#77), lock washer Ø8 (#76) and lock nut M8 (#38). Place 4 Rubber-Dampers (#88) and big flat washer Ø10 (#87) between the engine and mounting plate.

Step 8: Attach Ball Coupler

Attach the coupler (#89) to the tow bar by using two sets of hex bolt M12x120 (#90), flat washer Ø12 (#3) and lock nut M12 (#10).

15

Step 9: Attach Wheel Fenders

Attach the left & right wheel fender (#40 & 41) to the oil tank by using hex bolt M10x30 (#42), rubber washer (#46), flat washer Ø10 (#43), lock washer Ø10 (#45) and lock nut M10 (#44).

Step 10: Attach Hydraulic Hoses

- Place an O ring (#81) onto the exposed threads of the outlet connector. Then attach hose (#24) to outlet connector.

- Attach hose (#25) to the port on the oil tank. Place an O ring (#54) on the port and tighten the hose using Teflon tape.

- Attach the oil pipe (#85) to the other side of the gear pump with the clamp (#86)

16

Step 11: Attach Protection Tube

Insert the protection tube (#105) to the beam using hex bolt M10x45 (#55), big flat washer Ø10 (#87) and nylon lock nut M10 (#44).

17

LOG SPLITTER PARTS DRAWING

18

| Ref.No | Drawing No. | Description | Qty |
| --- | --- | --- | --- |
| 1 | LS22J-01000 | Beam Weldment | 1 |
| 2 | 9117-12055-DX12.9 | Screw M12x55 | 12 |
| 3 | 9301-12000-DX | Flat Washer Ø12 | 19 |
| 4 | 9306-12000-DX | Lock Washer Ø12 | 12 |
| 5 | 9210-12000-DX | Hex Thick Nut M12 | 12 |
| 6 | LSH22-00002-DY | Wedge Spacer | 2 |
| 7 | LSH22-00001-DY | Wedge Plate | 2 |
| 8 | LS22J-04000 | Wedge | 1 |
| 9 | 9101-08020-DX | Hex Bolt M8x20 | 1 |
| 10 | 9206-12000-DX | Hex Lock Nut M12 | 6 |
| 11 | 9306-18000-DX | Lock Washer Ø18 | 4 |
| 12 | 9301-18000-DX | Flat Washer Ø18 | 4 |
| 13 | 9201-18000-DX | Hex Nut M18 | 4 |
| 14 | N280-00043 | Adjustable Washer | several |
| 15 | LSH22-00004-DX | Valve A Joiner | 1 |
| 16 | 9905-00014 | Combination Washer Ø14 | 4 |
| 17 | LSH22-00005-DX | Bolt Connector | 2 |
| 18 | LSH22-00006 | Hydraulic Hose (Valve-Cylinder) | 1 |
| 19 | LSH22-06000 | Cylinder | 1 |
| 20 | LSA22-00009-DX | Front Cover Connector | 1 |
| 21 | 9901-16×2.5 | O Ring Ø16x2.5 | 1 |
| 22 | LSP25-17001 | Valve B Joiner | 1 |
| 23 | LSP25-17002 | Nut | 1 |
| 24 | LSH22-00008 | Hydraulic Hose (Valve-Pump) | 1 |
| 25 | LSH22-00007 | Hydraulic Hose (Valve-Oil Tank) | 1 |
| 26 | LSCA22-17001 | Control Valve | 1 |
| 27 | LSCA22-17002 | Spacer Plate | 1 |
| 28 | LSCA22-07003 | Handle | 2 |
| 29 | Z330-00002 | Plastic Handle Sleeve | 2 |
| 30 | C130-00004 | Nylon Washer | 4 |
| 31 | LSCA22-07200 | Frame Weldment | 1 |
| 32 | LSCA22-07100 | Connection Tube | 1 |
| 33 | 9110-08050-DX | Screw M8x50 | 2 |
| 34 | 9105-08016-FH | Inner Hex Screw M8x16 | 6 |
| 35 | 9101-08000-DX | Hex Nut M8 | 2 |
| 36 | 9403-05026-DX | Pin 5x26 | 1 |
| 37 | 9404-2X10/DX | Cotter Pin 2x10 | 1 |
| 38 | 9206-08000-DX | Hex Lock Nut M8 | 10 |
| 39 | 9302-08000-DX | Big Flat Washer Ø8 | 4 |
| 40 | LSA22-17000 | Left Fender | 1 |
| 41 | LSA22-18000 | Right Fender | 1 |
| 42 | 9101-10030-DX8.8 | Hex Bolt M10x30 | 6 |
| 43 | 9301-10000-DX | Flat Washer Ø10 | 7 |
| 44 | 9206-10000-DX | Hex Lock Nut M10 | 9 |

19

| Ref.No. | Drawing No. | Description | Qty |
| --- | --- | --- | --- |
| 45 | 9306-10000-DX | Lock Washer Ø10 | 6 |
| 46 | LSA22-00021 | Rubber Washer 2 | 6 |
| 47 | LSP25-00021 | Rubber Washer | 1 |
| 48 | LSP25-00022 | Filter | 1 |
| 49 | LSP25-15000 | Filter Fix Plate | 1 |
| 50 | LSP25-00010 | Oil Plug | 1 |
| 51 | LS22J-03000 | Oil Tank | 1 |
| 52 | LSP25-13000 | Oil Bolt | 1 |
| 53 | LSH22-00012-DX | Connector | 1 |
| 54 | 9901-14×2.5 | O Ring Ø14x2.5 | 2 |
| 55 | 9101-10045-DX8.8 | Hex Bolt M10x45 | 2 |
| 56 | LSA22-15000 | Rear Support Leg | 1 |
| 57 | LSH22-00003-DX | Wedge Pin | 1 |
| 58 | 9301-20000-DX | Flat Washer Ø20 | 2 |
| 59 | LSP25-00020-FH | Hex Slotted Nut M20 | 2 |
| 60 | 9404-04036-DX | Cotter Pin 4x36 | 2 |
| 61 | LSP25-00009-DX | Wheel Axle Cap | 2 |
| 62 | LS22J-00002 | Conical Hex Bolt M12x25x1.25 | 8 |
| 63 | LSP25-14000 | Wheel | 2 |
| 64 | LSP25-10007 | Gear Pump | 1 |
| 65 | LSP25-10005 | Gear Pump Stand | 1 |
| 66 | LSP25-10002-FH | Engine Connector | 1 |
| 67 | LSP25-10003-FH | Gear Pump Connector | 1 |
| 68 | LSP25-10006 | Connector Cover | 1 |
| 69 |  | Gear Pump Flat Key | 1 |
| 70 | 9101-08030-DX8.8q | Hex Bolt M8x30 | 4 |
| 71 | 9101-05010-DX8.9q | Hex Bolt M5x10 | 4 |
| 72 | LSP25-10008-FH | Wire Snap rings for shaft | 1 |
| 73 |  | Flat Key | 1 |
| 74 | Z330-00008-DX | Pawl | 2 |
| 75 | 9101-08025-DX8.8Q | Hex Bolt M8x25 | 4 |
| 76 | 9306-08000-DX | Lock Washer Ø8 | 18 |
| 77 | 9301-08000-DX | Flat Washer Ø8 | 8 |
| 78 | LSP25-10001 | Engine | 1 |
| 79 | LSP25-10004-DX | Engine Bushing | 1 |
| 80 | LSH22-08001 | Connector | 1 |
| 81 | 9901-11.2×2.4 | O Ring | 1 |
| 82 | 9101-06020-DX8.8q | Hex Bolt M6x20 | 6 |
| 83 | 9306-06000-DX | Lock Washer Ø6 | 6 |
| 84 | 9301-06000-DX | Flat Washer Ø6 | 6 |
| 85 | LSA22-00007 | Oil Pipe | 1 |
| 86 | LSP25-00011-BXG | Clamp | 2 |
| 87 | 9302-10000-DX | Big Flat Washer Ø10 | 6 |
| 88 | LSP25-00025 | Polyurethane Block | 4 |
| 89 | Z104 | 50mm Coupler | 1 |

20

| Ref.No | Drawing No. | Description | Qty |
| --- | --- | --- | --- |
| 90 | 9101-12120-DX8.8 | Hex Bolt M12x120 | 2 |
| 91 | LSA22-14000 | Front Pin | 1 |
| 92 | LSA22-12000 | Front Support Leg | 1 |
| 93 | T251-60000 | Handle Wheel | 1 |
| 94 | LSP25-00008-DX | Safety Pin | 1 |
| 95 | LSP25-00003 | Spring | 1 |
| 96 | 9404-03030-DX | Cotter Pin 3x30 | 1 |
| 97 | N021-00004 | R Pin | 2 |
| 98 | LSH22-02000 | Tow Bar | 1 |
| 99 | 9101-12040-DX8.8q | Hex Bolt M12x40 | 4 |
| 100 | LSA22-00015 | Hinge Pin | 1 |
| 101 | 9404-04040-DX | Cotter Pin 4x40 | 3 |
| 102 | LSA22-16000 | Handle Ring | 1 |
| 103 | 9101-10075-DX8.8 | Hex Bolt M10x75 | 1 |
| 104 | 9101-08075-DX8.8 | Hex Bolt M8x75 | 4 |
| 105 | LS22J-02100 | Clamp | 2 |
| 106 | LS22J-05000 | Cross Wedge | 1 |
| 107 | Z330-00003-FH | Spring B | 2 |
| 108 | Z330-00017-DX | Key Ring | 2 |
| 109 | LSH22-06009 | Piston Rod Connector | 1 |
| 110 | LSE22-00011 | Plastic Plug | 2 |
| 111 | 9121-06010-FH | Screw M6x10 | 1 |

21

Konformitätserklärung 
gemäß Maschinenrichtlinie 2006/42/EG, Anhang II A

EC-Declaration of Conformity according to machine directive 2006/42/EC, Annex II A

Hiermit erklären wir / We herewith declare

Jansen GmbH & Co. KG

Mühlenstr. 50

49824 Emlichheim

Dass die nachfolgend bezeichnete Maschine(n) aufgrund Ihrer Bauart mit den grundlegenden Sicherheits- und Gesundheitsanforderungen der einschlägigen EG-Richtlinien übereinstimmen.

That the following machine(s), based on its construction, comply with the basic safety and health requirements of the appropriate EC-directives.

Maschinenbeschreibung & Typ:

Description of machine:

Holzspalter / log splitter:  LS22J

Verkaufsbezeichnung / sales designation:  HS-22A62

die Konformität mit folgenden EG-Richtlinien / conformity tot he following EC directive:

-	2006/42/EG	EG-Maschinenrichtlinie

-	2006/95/EG 	Niederspannungsrichtlinie vom 12. Dezember 2006

-	2004/108/EG 	EMV-Richtlinie vom 15. Dezember 2004

Angewandte harmonisierte Normen / Applicable EC directives:

-	EN ISO 12100-1:2003; Sicherheit von Maschinen — Grundbegriffe, allgemeine Gestaltungsleitsätze — Teil 1: Grundsätzliche Terminologie, Methodologie

-	EN ISO 12100-2:2003; Sicherheit von Maschinen — Grundbegriffe, allgemeine Gestaltungsleitsätze — Teil 2: Technische Leitsätze

Person, die bevollmächtigt ist, die technischen Unterlagen zusammenzustellen:

Name, title, date and signature of responsible person:

G. Kuipers,  Fa. Jansen GmbH & Co. KG

Emlichheim,  05.07.2018

G. Kuipers, Geschäftsführer

# Text boxes

###### DANGER

###### WARNING

###### CAUTION

###### CAUTION

22TON

23 Seconds

2.5 Gallons or at the middle of the Oil Cup

24inches

150Lbs(68kgs)

50 mm

16 inches

25KM/H

196CC, OHV, 4stroke

4-1/2” x 23”

10W AW32, ASLE H-150, ISO 32

2-Stage

3500 psi

8 GPM

Detent (auto-return)

88”L x 40”W x 45”H

Ram Force………………………….

Cycle Time ………………………...

Hydraulic Tank Capacity …………..

Max. Log Length…………………...

Max. Log Weight…………………...

Coupler Ball Size ………………….

Tire Size……………………………

Max. Towing Speed…………...........

Engine………………………………

Cylinder Size …………....................

Hydraulic Fluid Type …………........

Gear Pump …………………………

Max. Pressure ……………………...

Max. Flow Capacity…………..........

Control Valve……………………….

Overall Dimensions………………...

Hydraulic Oil

Use types 10W AW32, ASLE H-150, and ISO32

The manufacturer reserves the right to make improvements in design and/or changes in specifications at any time without incurring any obligation to install them on units previously sold.

22

PLEASE NOTE:

BEFORE REMOWING VALVE SPOOL OR SPOOL

SLEEVE REMOVE DETENT ADJUSTING CART,

DETENT PISTON AND STEEL BALL.INSTALL

SPOOL AND SPOOL SLEEVE BEFORE

REINSTALL STEEL BALL.

PRESSURE RELEASE DETENT

This feature provides a pressure release detent for the spool “out” (handle in ) position. When the spool is manually placed in the detent position oil is directed to the “B” work port reaches a preset level the detent will release and the spool will center. The factory setting is 1400psi.The detent release pressure is adjustable by loosening the jam nut and turning the adjusting screw. Turning the adjusting screw clockwise will increase the detent release pressure and counterclockwise will decrease the detent release pressure. NOTE: if the detent release pressure is set too high the spool will not center, if the pressure is too low the detent will not hold. If cap screw item 6 becomes loose detent will not function properly.

RELIEF VALVE

An adjustable ball spring relief valve is standard on all valves. The factory setting is 3000psi, 3gpm and 120ºF.

Other settings can be specified.

The relief pressure is adjusted by removing nut, and turning the adjusting screw. Turning the adjusting screw clockwise will increase the pressure and counterclockwise will decrease the pressure (a pressure gauge must be installed in the inlet line whenever the relief pressure is adjusted). Do not backout

adjusting screw to the point it falls out.

WARNING: OVERPRESSURE MAY CAUSE SUDDEN AND UNEXPECTED FAILURE OF A COMPONENT IN THE HYDRAULIC SYSTEM RESULTING IN SERIOUS PERSONAL INJURY.ALWAYS USE A GAUGE WHEN ADJUSTING A RELIEF VALVE.

ITEM      QTY    DESCRIPTION

1         1      sleeve

2         1      handle

3         4      inner hex screw

4         1      end cap

5         1      cotter pin

6         1      link

7         1      pin

8         1      valve core

9         2      ring

10        2      rubber ring

11        2      o-ring

12        1      plug screw

13        1      o-ring

14        1      adjusting screw

15        1      adjusting spring

16        1      seat

17        1      steel ball

18        1      screw sleeve

19        1      valve

20        2      ring

21        1      return spring

22        1      guide sleeve

23        1      locating sleeve

24        1      rubber washer

25        1      o-ring

26        1      sliding valve core

27        1      o-ring

28        1      round pin

29        4      steel ball

30        1      screw

31        1      push rod

32        1      steel ball

33        1      adjusting spring

34        1      adjusting screw

35        1      protection sleeve

36        1      locating sleeve

37        1      plastic cover

23